## Slide 1
COMP4601 • FINAL PROJECT PRESENTATION • KRIA KV260
FPGA Acceleration of
JPEG-Style Grayscale
Image Compression
512×512 PGM
FPGA
K26 PL
DCT • Q • RLE
custom packed
output
Abhishek Poddar z5581147
Sakina Huzaifa z5400462
Krishna Mittal z5625451
Shriya Malik z5619441
Notes: This project investigates whether a JPEG-style grayscale image compressor can be accelerated on the programmable logic of the Kria KV260. The complete compression path uses 8 by 8 blocks, level shifting, a two-dimensional discrete cosine transform, quantisation, zigzag traversal, and packed run-length encoding. We benchmarked the implementation on 41 fixed 512 by 512 PGM images: 30 supplied natural images and 11 deterministic synthetic stress tests. The most important result is deliberately stated on the title slide. The FPGA did accelerate the arithmetic stages that looked expensive in the CPU profile. The DCT became about 1.22 times faster, and quantisation became about 5.18 times faster. However, the variable-length encoding stage consumed nearly 78 percent of FPGA kernel time. Therefore, the complete FPGA kernel averaged 42.65 milliseconds per image, while the CPU completed the full software run in 33.26 milliseconds. This is still a valuable engineering result. It demonstrates a complete working accelerator, preserves essentially the same compression effectiveness, and identifies the real bottleneck for the next design iteration.

## Slide 2
COMP4601 • FINAL PROJECT PRESENTATION • KRIA KV260
Can Kria KV260 improve the performance of the complete compression workload?
A complete 8×8 DCT, quantisation, zigzag and packed RLE pipeline — profiled across 41 images on the KV260.
Headline result
DCT and quantisation improved — but serial entropy coding made the current FPGA kernel slower overall.
512×512 PGM
FPGA
K26 PL
DCT • Q • RLE
custom packed
output
41
benchmark images
30 natural + 11 synthetic
4.07:1
aggregate FPGA ratio
10.75 MB → 2.64 MB
5.18×
quantisation speedup
largest arithmetic-stage gain
77.9%
kernel time in encoding
the dominant bottleneck
Source: project CPU console outut and hardware_stage_profile.cv.
Notes: This project investigates whether a JPEG-style grayscale image compressor can be accelerated on the programmable logic of the Kria KV260. The complete compression path uses 8 by 8 blocks, level shifting, a two-dimensional discrete cosine transform, quantisation, zigzag traversal, and packed run-length encoding. We benchmarked the implementation on 41 fixed 512 by 512 PGM images: 30 supplied natural images and 11 deterministic synthetic stress tests. The most important result is deliberately stated on the title slide. The FPGA did accelerate the arithmetic stages that looked expensive in the CPU profile. The DCT became about 1.22 times faster, and quantisation became about 5.18 times faster. However, the variable-length encoding stage consumed nearly 78 percent of FPGA kernel time. Therefore, the complete FPGA kernel averaged 42.65 milliseconds per image, while the CPU completed the full software run in 33.26 milliseconds. This is still a valuable engineering result. It demonstrates a complete working accelerator, preserves essentially the same compression effectiveness, and identifies the real bottleneck for the next design iteration.

## Slide 3
PROJECT OVERVIEW
What we set out to build — and how success was judged
The goal was not only to move code into hardware, but to improve the complete compression workload.
Problem
Image compression contains both regular arithmetic and irregular variable-length coding. The first is naturally parallel; the second is much harder to map efficiently to an FPGA.
1
Accelerate the full compressor
Implement the 8×8 processing pipeline in Vitis HLS and run it on the KV260 programmable logic.
2
Preserve useful compression
Compare total compressed size and compression ratio across the identical 41-image suite.
3
Measure the whole system
Profile individual stages, transfer overheads and file I/O — not only HLS latency.
Scope
512×512
8-bit PGM P5
4,096
8×8 blocks/image
167,936
blocks in suite
Outcome snapshot
Worked
Complete 41-image hardware run; arithmetic stages accelerated; compression ratio retained.
Did not
The current full FPGA implementation did not beat the CPU because packed encoding remained serial.
SUCCESS = SYSTEM-LEVEL SPEEDUP
Notes: Our project aim was broader than accelerating one mathematical function. We wanted a complete image-compression solution that could read an image, process every 8 by 8 block, produce a compact encoded output, and be measured fairly against a software baseline. Each input is a 512 by 512, 8-bit binary PGM image. That gives 262,144 pixels and 4,096 blocks per image. Across the 41-image benchmark, the system processed 167,936 blocks. We included both natural images and synthetic patterns because compression algorithms behave very differently on smooth, repetitive and noisy content. We defined success using three criteria. First, the accelerator had to complete the entire compression pipeline rather than only DCT or quantisation. Second, compressed size had to remain useful and comparable to the CPU baseline. Third, performance evaluation had to include stage-level measurements and data movement, so that a large kernel-only number could not hide application overhead. The outcome is mixed but informative. The hardware implementation completed the full benchmark and improved the regular arithmetic stages. Compression effectiveness was essentially maintained. The missing objective was full-system speedup, and the measurements clearly explain why.

## Slide 4
DESIGN — ALGORITHM
How the JPEG-style compression pipeline works
The compressor removes visual redundancy first, then represents the remaining information compactly.
1
Level shift
pixel − 128
Centre values around zero
2
2D DCT
F = CXCᵀ
Convert pixels to frequencies
3
Quantise
round(F / Q)
Discard fine detail; create zeros
4
Zigzag
low → high f
Move likely zeros together
5
RUN/SIZE
ZRL + EOB
Encode zero runs and values
6
Packed file
GSC3 bytes
Write compact block stream
Why compression emerges
•
Energy concentration
The DCT places most visible structure in a small number of low-frequency coefficients.
•
Sparsity
Quantisation rounds many high-frequency coefficients to zero, especially in smooth blocks.
•
Compact coding
Zigzag scanning groups zeros so RUN/SIZE symbols and EOB markers use fewer bits.
Lossy step
Quantisation is the intentional quality–compression trade-off. All later stages preserve the quantised coefficients.
Notes: The algorithm follows the main ideas used in JPEG, adapted to grayscale PGM images and a custom packed output format. Each image is divided into 8 by 8 blocks. First, subtracting 128 moves the unsigned pixel range around zero, which is convenient for the transform. The two-dimensional DCT then converts the block from 64 pixel values into 64 frequency coefficients. Low frequencies describe smooth brightness changes, while high frequencies describe sharp detail. The DCT itself does not compress the data. Its purpose is to concentrate visually important information into fewer coefficients. Quantisation is the lossy stage. Each coefficient is divided by a value from a quantisation matrix and rounded. High-frequency coefficients use larger divisors and therefore frequently become zero. Zigzag traversal then visits low frequencies first and high frequencies later, so these zeros form long consecutive runs. Finally, the encoder stores the DC coefficient separately and represents AC coefficients using JPEG-style RUN and SIZE symbols, including zero-run-length and end-of-block markers. The symbols and amplitudes are packed into bytes. The key design tension is visible here: DCT and quantisation have fixed work for every block, but the encoder performs data-dependent work based on how many non-zero coefficients remain.

## Slide 5
DESIGN — ARCHITECTURE
Hardware/software partitioning on the Kria KV260
Linux and XRT manage files and buffers; the programmable logic executes the block-compression kernel.
Processing system (ARM/Linux)
SOFTWARE
Read PGM P5
Parse header and pixels
Prepare buffers
Copy or pack image data
Control accelerator
XRT launch and synchronization
Write GSC3 file
Store metadata and packed bytes
Record metrics
CSV timing and status
DDR / AXI
Input pixels
Output DC + bit counts
Packed AC bytes
Programmable logic — full-image compression kernel
VITIS HLS
Load + shift
Separable DCT
Quantise
Zigzag + encode
Nested block traversal: 64 × 64 = 4,096 blocks per image
AXI-Lite control
kernel arguments + start/status
m_axi data ports
burst reads/writes to memory
Output checks
size + status flags
compressed metadata + payload
Notes: The design is split between the processing system and the programmable logic. The ARM processor runs Linux and handles the tasks that are awkward or unnecessary to synthesize: reading PGM files, allocating XRT buffers, launching the kernel, synchronising transfers, writing the compressed file and recording measurements. The image pixels and output arrays reside in shared external memory. AXI master interfaces move the large data buffers, while AXI-Lite carries control arguments and kernel status. The hardware kernel receives the full image and iterates over all 4,096 blocks. For each block it loads and level-shifts the pixels, performs the separable DCT, quantises the coefficients, traverses them in standard zigzag order, and produces a packed AC bitstream together with the DC value and valid bit count. This partition keeps file-system code and dynamic host control in software, while the regular inner computation is implemented as a dedicated datapath. It also makes performance interpretation important: the kernel can be measured separately, but an application still pays for loading, host preparation, host-to-device transfer, device-to-host transfer and file writing. The HLS configuration requested a 200 megahertz clock, but the presentation does not claim post-route timing or resource results because those reports were not part of the supplied benchmark data.

## Slide 6
DESIGN — HLS IMPLEMENTATION
Where parallelism was introduced — and where it was not
The datapath is highly parallel inside each 8×8 transform, but output generation remains data dependent.
Fixed-point datapath
LOWER OPERATOR COST
Pixels use 9-bit signed values; DCT intermediates use carefully sized fixed-point types; quantised coefficients use 16-bit integers.
Separable 8×8 DCT
128 DOT PRODUCTS
Two one-dimensional matrix passes replace a direct 2D calculation and expose regular multiply–accumulate structure.
Partition + unroll
PARALLEL INNER SUMS
8×8 local arrays are fully partitioned; each eight-term DCT reduction is fully unrolled; output loops are pipelined at II=1.
Packed encoder
VARIABLE LENGTH
Standard zigzag, RUN/SIZE, ZRL and EOB symbols are packed into bytes with per-block status checks.
Conceptual schedule inside one block
Load + shift
DCT pass 1
DCT pass 2
Quantise
Encode bytes
Fixed-work arithmetic can be scheduled predictably.
Encoder work expands with the number of emitted symbols and bytes.
Remaining serial constraints
TARGET 200 MHz
•
Block traversal
The current kernel processes blocks through one top-level nested loop.
•
Bitstream construction
RUN/SIZE emission and packed byte writes depend on coefficient content.
Notes: The HLS implementation contains several deliberate optimisations. Floating-point arithmetic was replaced with fixed-point and integer types sized for the pixel, intermediate DCT and quantised coefficient ranges. This reduces operator cost and gives HLS more predictable hardware. The DCT is separable. Instead of calculating every output directly from all 64 pixels, the design performs two sets of one-dimensional transforms. Local 8 by 8 arrays are fully partitioned, so values can be read in parallel. The eight-term inner sums are fully unrolled, and the surrounding output loops are pipelined with an initiation interval of one. These choices are exactly why the DCT and quantisation stages show real acceleration in the measurements. The entropy coder is more difficult. Zigzag lookup is regular, but the number of zeros, non-zero coefficients, zero-run markers, amplitude bits and output bytes changes from block to block. The current design therefore builds each variable-length stream sequentially and writes the valid bytes for one block before continuing. The conceptual schedule at the bottom highlights the difference. Arithmetic stages have a known amount of work and can be deeply scheduled. Encoding grows with data complexity, so its execution time tracks compressed output size. This limitation becomes the central result of the performance analysis.

## Slide 7
RESULTS — METHOD
How the CPU and FPGA measurements were collected
The comparison uses identical 512×512 images and per-stage averages rather than a single headline latency.
Benchmark protocol
•
Dataset
30 natural images plus 11 synthetic edge cases; every file is 512×512 PGM P5.
•
CPU baseline
One complete software batch with stage-level profiling; 41 images and 167,936 blocks.
•
FPGA profiling
One warm-up followed by 10 timed runs per image; average, minimum and maximum recorded.
•
Metrics
Compressed bytes, compression ratio, load/shift, DCT, quantise, encode, transfers, file writing and status.
ratio = raw bytes / compressed bytes speedup = CPU time / FPGA time
CPU BASELINE EVIDENCE
33.260 ms
CPU total / image
4.042:1
CPU aggregate ratio
Notes: The evaluation was designed to avoid comparing incompatible numbers. Every image in the accelerated CSV is 512 by 512 and therefore contains the same number of pixels and blocks. The suite combines natural images with synthetic patterns such as flat fields, gradients, checkerboards, an impulse and fixed-seed random noise. The CPU screenshot records a complete batch of 41 images. It reports the total compressed size, overall compression ratio and average time spent in image loading, level shifting, DCT, quantisation, zigzag, RLE and bit encoding, file writing and other overhead. Its average complete time is 33.260 milliseconds per image. For hardware, each row reports one warm-up and ten timed runs. We use the average stage fields for load and shift, DCT, quantisation, encoding and total kernel time. Minimum and maximum values are also retained to check stability. Host loading, copy, transfer and file-writing fields let us estimate a single application run. One important caveat is shown explicitly. The raw end-to-end field in the supplied CSV is a cumulative profiling-session measurement rather than a per-run application latency. We therefore do not divide the CPU time by that field. Instead, comparisons use the per-run averages and, where an application estimate is needed, add one load, host copy, transfer, kernel, return transfer and file write.

## Slide 8
RESULTS — COMPRESSION
Compression effectiveness was essentially preserved
Output size depends strongly on image structure, but the aggregate CPU and FPGA ratios remain very close.
4.042:1
CPU aggregate ratio
2,659,049 compressed bytes
4.072:1
FPGA aggregate ratio
2,639,243 compressed bytes
0.74%
smaller FPGA output
difference is small, not bit-identical
41 / 41
successful status
status = 0 for every image
What the distribution means
•
Highly regular images
Flat and repetitive patterns reached 12.71:1 because quantisation produced long zero runs.
•
Natural images
The median result was 4.38:1, reflecting mixed smooth areas, edges and texture.
•
Random noise
fixed_seed_noise reached only 1.09:1 because most high-frequency coefficients remained non-zero.
Notes: Before discussing speed, we first check whether the accelerator still performs useful compression. The CPU baseline compressed 10,747,904 raw bytes to 2,659,049 bytes, which is an overall ratio of 4.042 to one. The hardware profile compressed the same total raw size to 2,639,243 bytes, giving 4.072 to one. The hardware output is about 0.75 percent smaller. This difference is small, but it also means we should describe the implementations as having essentially the same compression effectiveness rather than claiming bit-identical output. All 41 accelerated rows report status zero, so the benchmark completed successfully for every input. The sorted chart shows why a single average ratio does not tell the whole story. Uniform and strongly repetitive synthetic images reach 12.71 to one. Natural images occupy the middle of the range, with a median of 4.38 to one. Fixed-seed random noise compresses to only 1.09 to one because random pixel changes create high-frequency DCT coefficients throughout the block. Quantisation cannot turn many of those coefficients into zero, so the encoder must emit far more symbols and bytes. This data dependence is expected for transform compression, but it also becomes a performance issue because the FPGA encoder performs more work when the compressed output is larger.

## Slide 9
RESULTS — PERFORMANCE
The arithmetic accelerated, but the complete FPGA pipeline did not
CPU and FPGA stage times reveal exactly where the gains were lost.
Average stage time per 512×512 image
Longer bar = more time. Speedup above 1× is faster on FPGA.
Level shift
CPU
FPGA
1.158 ms
1.552 ms
0.75×
2D DCT
CPU
FPGA
7.760 ms
6.361 ms
1.22×
Quantisation
CPU
FPGA
7.724 ms
1.491 ms
5.18×
Zigzag + coding
CPU
FPGA
12.402 ms
33.239 ms
0.37×
CPU coding combines zigzag scan (3.530 ms) and RLE/bit encoding (8.872 ms).
Whole-pipeline view
33.26 ms
CPU complete run
42.65 ms
FPGA kernel only
48.08 ms
estimated FPGA app path
0.78×
kernel vs CPU total
0.69×
estimated app vs CPU
Notes: This slide is the main performance comparison. The stage bars use average milliseconds per image. Level shifting is slightly slower in hardware, giving a speedup below one. The DCT improves from 7.760 milliseconds on the CPU to 6.361 milliseconds in the FPGA, or about 1.22 times faster. Quantisation is the strongest result: 7.724 milliseconds becomes 1.491 milliseconds, a 5.18 times acceleration. For coding, the CPU values for zigzag and RLE are combined because the FPGA CSV reports a single encode stage. The CPU requires 12.402 milliseconds, while the FPGA requires 33.239 milliseconds. That is only 0.37 times the CPU performance, or about 2.68 times slower. This single loss is larger than the savings from DCT and quantisation. The whole-pipeline cards make the consequence clear. The CPU complete run is 33.26 milliseconds. The FPGA kernel alone is 42.65 milliseconds, so even before transfers and file operations it is about 28 percent slower. Adding one average PGM load, host copy, H2D transfer, kernel run, D2H transfer and file write gives an estimated application path of 48.08 milliseconds. Therefore, the correct conclusion is not that FPGA acceleration failed generally. The arithmetic datapath worked. The architecture failed to accelerate the dominant variable-length stage.

## Slide 10
DISCUSSION
Why the packed encoder became the system bottleneck
The more bytes an image produces, the longer the FPGA spends emitting its variable-length stream.
Compute-stage composition
Comparing only level shift, DCT, quantisation and coding
CPU
26.7%
26.6%
42.7%
FPGA
77.9%
load/shift
DCT
quantise
encode
77.9%
FPGA kernel in encode
0.03%
mean min–max spread
The timing is stable. The bottleneck is architectural, not measurement noise.
Compressed size explains encoding time almost perfectly (r = 0.9995): more symbols and bytes create more serial packing work.
Notes: The bottleneck analysis compares the composition of the fixed compute stages. On the CPU, coding accounts for about 42.7 percent of level shift, DCT, quantisation and entropy-coding time. In the FPGA kernel, encoding expands to approximately 77.9 percent. DCT and quantisation occupy much smaller shares because those stages were successfully parallelised. The scatter plot provides stronger evidence than a single average. Each point is one image, with compressed output size on the horizontal axis and FPGA encoding time on the vertical axis. The correlation is 0.9995, which is almost perfect. Uniform images produce about 20 kilobytes and take roughly 18.46 milliseconds to encode. The fixed-seed noise image produces about 235 kilobytes and takes about 96.08 milliseconds. This relationship indicates that the encoder performs work proportional to the number of symbols and bytes it emits. A serial bit writer, repeated zero-run decisions and per-byte output loops therefore dominate complex images. The result is not caused by unstable profiling. Across the ten timed runs, the average minimum-to-maximum spread for total kernel time is only about 0.03 percent. The measurements are highly repeatable. The next design should therefore change the encoder architecture rather than simply collect more repetitions or make small changes to the already-fast DCT and quantisation stages.

## Slide 11
CONCLUSION
What worked, what did not — and what we would change next
The project’s main lesson is that end-to-end acceleration depends on the slowest stage after optimisation.
What worked
✓
Complete FPGA pipeline
All 41 images completed with successful status and a custom packed output.
✓
Arithmetic acceleration
DCT improved by 1.22× and quantisation by 5.18×.
✓
Compression retained
Aggregate ratio remained close: 4.042:1 CPU versus 4.072:1 FPGA.
What did not
!
No full-system speedup
42.65 ms kernel-only versus 33.26 ms for the CPU complete run.
!
Serial packed encoding
Variable-length output consumed 77.9% of kernel time.
!
Limited parallel workload
One block stream and fixed output loops constrained throughput.
Given more time
1
Redesign the writer
Use a byte reservoir and emit whole codewords rather than one bit at a time.
2
Move only valid output
Create a compact contiguous AC stream; avoid fixed-slot byte transfers.
3
Exploit coarse parallelism
Add DATAFLOW, multiple block/CU lanes and batch images to amortise transfers.
Next-iteration roadmap
01
Byte-reservoir coder
02
Compact output stream
03
DATAFLOW between stages
04
Parallel blocks / CUs
05
Post-route power + timing
Final takeaway: accelerating the obvious arithmetic is not enough — the architecture must be designed around the bottleneck that remains.
Notes: The project achieved several important objectives. We implemented a complete FPGA compression pipeline and successfully processed all 41 benchmark images. The DCT and quantisation results confirm that fixed-point arithmetic, array partitioning, unrolling and pipelining can accelerate regular image-processing stages. The aggregate compression ratio stayed essentially unchanged, so the accelerated path remained useful as a compressor. The main objective that was not achieved is end-to-end speedup. The current kernel is slower than the complete CPU baseline because packed variable-length encoding became dominant. This is a classic optimisation effect: once the arithmetic stages improve, the bottleneck moves to a stage that previously looked less important. With more time, the first priority would be a new encoder. A byte reservoir should append complete symbols and amplitudes rather than writing one bit per loop iteration. Output should be compact and contiguous so only valid bytes are transferred. DATAFLOW could overlap load, transform, quantisation and encoding where dependencies allow. Multiple block lanes or compute units could process independent image regions, and batching several images could amortise launch and transfer overhead. Finally, a complete engineering evaluation would add post-route timing closure, FPGA resource utilisation, board power and energy per image. The central conclusion is that successful acceleration requires designing for the entire pipeline and its data movement, not only the mathematically expensive stage.